## Slide 1
KLA i4C HACKATHON · PROBLEM STATEMENT PS01
DrishtiNet
दृष्टि
Adaptive, degradation-aware restoration of degraded semiconductor inspection images
TEAM DETAILS
Member name | Role in team | Focus area
[ Name 1 ] | Lead architect | Model design, training runs, experiment ladder
[ Name 2 ] | Data / loss engineer | Degradation engine, FabLoss, Day-0 audit
[ Name 3 ] | Deployment & benchmarking | eval.py, FP16/ONNX, timing harness
[ Name 4 ] | Validation & narrative | Metric suite, LODO, visuals, deck
Registration
Team name: [ team name ]
College: [ institute ]
City: [ city ]
Contact: [ email / phone ]
Track: KLA — PS01 (image restoration)
Submission format: PDF, file name TeamName_KLA_PS01 · 9 slides (this deck) · public GitHub repo linked on slide 8
DRISHTI-Net · KLA i4C Hackathon · PS01
1 / 9

## Slide 2
Problem statement — why this matters
AI-based restoration of degraded images for semiconductor inspection (KLA, PS01)
DRISHTI-Net · KLA i4C Hackathon · PS01
2 / 9
• One pixel can hide a defect. Inspection images drive pass/fail decisions at every fab stage; a speckle spike or a lost line edge can mask a killer defect and ship a bad die.
• Real inspection images arrive degraded. Random speckle, a soft Gaussian haze, and 2× downsampling (512²→256², 256²→128²) jointly destroy signal. These losses occur together, not one at a time.
• Engineers currently just live with it. Every fab pays for degraded data in escapes and re-measurements. Restoration that recovers the true image is direct yield value.
• The catch: the test set is out-of-distribution. Winning requires generalizing to unseen image sources — and doing it fast enough to inline with fab throughput.
Speckle noise
Random, grainy, multiplicative — pushes pixels BEYOND the true intensity range.
Must fix: Denoise without blurring away real structure.
Gaussian degradation
Soft, hazy, edges lose sharpness — blur and/or additive noise.
Must fix: Restore edge sharpness; no ringing artifacts.
2× resolution loss
512²→256² or 256²→128² downsampled; fine detail gone.
Must fix: Reconstruct missing detail while upscaling 2×.
The trap designed into this PS: degraded intensities can exceed the ground-truth range. Any pipeline that clips or min-max normalizes destroys exactly the information it was asked to protect.

## Slide 3
Idea description — read it, restore it, protect it
One model. One forward pass. All three degradations handled jointly.
DRISHTI-Net · KLA i4C Hackathon · PS01
3 / 9
“DRISHTI-Net reads the corruption before repairing it: a degradation encoder — supervised by ground-truth parameters from a 10,000-variant synthetic degradation engine — modulates a NAFNet backbone so every layer adapts its filter strength to the damage it sees, while a defect-weighted loss protects the edges semiconductor inspection depends on.”
1 · Read the corruption
• Tiny CNN encodes the input into a 64-d latent z — an implicit fingerprint of the degradation
• Auxiliary head is supervised with the true σ-speckle, σ-blur and kernel used to build each training pair
• Result: adaptivity that is trained, verifiable, and demo-able
2 · Restore adaptively
• z modulates every NAFBlock via FiLM (scale + shift): noise-heavy → stronger denoise, blur-heavy → stronger deblur
• One joint pass does denoise + deblur + 2× super-resolution — no cascade, no information loss between stages
• PixelShuffle learned upsampling; ~3.5M params, FP16-friendly
3 · Protect the patterns
• Pixel loss weighted by ground-truth edge magnitude — pattern borders get 2–3× optimizer attention
• Sobel + frequency losses preserve line edges and periodic grating structures
• Deterministic regression, not a generative prior — output is a direct estimate, minimizing the risk of synthesizing unsupported structure
Deliberately absent: diffusion / GAN (hallucination risk + fails the latency benchmark), Mixture-of-Experts and hard routing (training instability, branching latency), Mamba/SSM kernels (toolchain risk on a clean benchmark machine).
In inspection, a fabricated edge is a false defect and a smoothed scratch is an escape — we chose determinism.

## Slide 4
Proposed solution — architecture & training system
Supervised degradation conditioning · metric-aligned loss · synthetic OOD engine
DRISHTI-Net · KLA i4C Hackathon · PS01
4 / 9
Input
128² / 256²
float32, native range
Input encoding
[x/S , log1p(x/S)]
2 channels · no clipping
S fixed on Day 0
Degradation encoder
3×conv + GAP → z∈R⁶⁴
aux head predicts true
σ-speckle / σ-blur / kernel*
FiLM-conditioned NAFNet
enc [2,2,4] → mid 4 → dec [2,2,2]
SimpleGate + SCA + LayerNorm
FiLM(z) in every block · no BatchNorm
skip-add at 3 scales
PixelShuffle ×2
conv 32→128 · shuffle
conv 32→1
+ bilinear global residual
Restored output
256² / 512²
GT dtype & range
exact inversion
* aux head trains the encoder on synthetic pairs only (real KLA pairs carry no degradation labels — masked). z-modulation is invisible to the benchmark: FiLM adds < 1% latency.
FabLoss — the metrology-aligned loss
L = L_DW-Charb + 0.5·(1 − MS-SSIM) + 0.2·L_Sobel + 0.1·L_FFT + 0.05·L_aux (synthetic only)
• DW-Charbonnier — robust pSNR base; pixels near GT edges weigh 1–3× (defect preservation is literal optimization)
• MS-SSIM — optimizes the judged metric directly
• Sobel edge — locks critical-dimension line edges · FFT-L1 — recovers periodic grating frequency content
• aux — supervises the degradation encoder (known synthetic parameters)
Every λ is fixed by our ablation ladder, never assumed.
Synthetic degradation engine — our OOD weapon
New randomized pair from clean GT every epoch:
• Speckle multiplicative — unclipped (may exceed range)
• Gaussian blur σ∈[0.5, 2.5] + additive noise (both — brief is ambiguous)
• Downsample kernel ×4 (bilinear/bicubic/area/lanczos)
• Random degradation order · CutBlur · D4 symmetries
• Instrument artifacts: scan-line jitter, column banding, edge bloom
We learn the degradation process, not the training images.

## Slide 5
Innovation & uniqueness — five claims, each with evidence
Novelty that survives cross-examination: every claim pairs with a measured proof
DRISHTI-Net · KLA i4C Hackathon · PS01
5 / 9
1
Supervised implicit degradation encoding
A latent fingerprint of the corruption — trained with the true parameters of every synthetic pair, so adaptivity is verifiable, not claimed.
Proof: live read-out of estimated σ-speckle / σ-blur / kernel on a degraded sample
2
FiLM conditioning — adaptive without routing
One model that behaves like many: degradation-conditioned scale/shift in all 28 blocks. None of the instability of MoE or cascades.
Proof: ablation ladder — Model 2 vs Model 1 ΔpSNR / ΔSSIM
3
Defect-weighted metrology optimization
Charbonnier weighted by GT edge magnitude (α=2): the optimizer spends capacity on line edges and contours, not flat background.
Proof: edge-region pSNR & Edge-SSIM gains, Model 4 vs Model 3
4
Instrument-aware synthetic OOD engine
10,000+ randomized speckle/blur/kernel/order combinations plus scan-jitter, banding and bloom artifacts of real inspection tools.
Proof: LODO benchmark — pSNR on degradation corners never seen in training
5
Deterministic, anti-hallucination design
A deterministic reconstruction objective rather than a generative prior — minimizing the risk of synthesizing unsupported structures (or erasing real ones). Built for metrology, not for pretty pictures.
Proof: flat-region hallucination penalty + worst-patch SSIM metrics
Also engineered in: fixed-scale no-clip input with log1p homomorphic channel · LODO OOD validation protocol · worst-patch quality metrics · benchmark-hardened eval script.

## Slide 6
Results — measured, not promised
Every number on this slide is produced by our own evaluation harness on held-out splits. No estimates.
DRISHTI-Net · KLA i4C Hackathon · PS01
6 / 9
Validation split | pSNR ↑ | SSIM ↑ | LPIPS ↓ | Edge-SSIM ↑
In-distribution val | pending | pending | pending | pending
LODO — unseen degradations | pending | pending | pending | pending
Worst-10% patches (64²) | pending | pending | pending | pending
Populated after the Day-4 training gate. Extended tables add edge-region pSNR and flat-region hallucination penalty.
Measurement protocol
• Timing: FP16, 10-iter warmup, CUDA-sync, median of ≥100 runs
• LODO split = degradation corners excluded from training
• Worst-patch: 64×64 windows, stride 32 — no hiding blur behind global averages
• Same script KLA will run (eval.py), same machine class (H100)
image panel after Day-4
Degraded input
noisy · low-res 256 × 256
image panel after Day-4
DRISHTI-Net output
restored 512 × 512
image panel after Day-4
Ground truth
clean · full-res 512 × 512
Panels and the degradation-estimate demo (model reading σ-speckle / blur / kernel off a real input) are inserted straight from eval outputs.

## Slide 7
Technology & feasibility
Small model, standard stack, reproducible by design
DRISHTI-Net · KLA i4C Hackathon · PS01
7 / 9
Stack & numbers
Framework
PyTorch 2.x, bf16 mixed-precision training
Data engine
OpenCV + NumPy, on-the-fly synthetic pairs
Model size
≈ 3.5 M params, ~14 MB fp32 (measured at build)
Inference
single pass, FP16; ONNX → TensorRT export path
Latency
pending timing harness — median ≥100 runs on GPU
Training HW
[ our GPU / Colab / cloud — fill in ]
Eval script
zero-edit CLI; auto CUDA→CPU; dtype-preserving
Reproducibility
requirements.txt · fresh-clone run gate before submit
Why this is feasible — and disciplined
• ~3.5 M-param CNN trains in hours, not days — full experiment ladder fits the schedule
• Ladder discipline: M0 baseline → M1 engine → M2 conditioning → M3 losses → M4 defect-weighting → M5 hardening; each step must beat the last or it is cut
• 128²-px training crops, EMA, cosine LR — converges on a single mid-range GPU
• Fall-back safety: eval.py runs on CPU if CUDA is absent on the scoring machine
Execution plan
D0
data audit
D1
engine + scaffold
D2
M0–M2 train
D3
loss ablations
D4
LODO + OOD
D5
speed + eval.py
D6
deck + repo
Hard vetoes: diffusion · MoE/hard routing · Mamba · gradient-TTA · clipping normalization · BatchNorm · any unmeasured number.

## Slide 8
GitHub repository & demo
A reviewer clones the repo and runs inference without contacting us
DRISHTI-Net · KLA i4C Hackathon · PS01
8 / 9
Repository — github.com/[team]/drishti-net
├── models/ # DRISHTI-Net architecture
├── data/ # degradation engine + loaders
├── losses/ # FabLoss (DW-Charb, MS-SSIM, Sobel, FFT)
├── utils/ # metric suite, LODO splits, timing
├── evaluate.py # MANDATORY: zero-edit CLI inference
├── train.py # full ladder: M0 → M5
├── weights/ # final checkpoint (Git-LFS / HF link)
├── outputs/ # our restored images on the test set
├── requirements.txt # exact pip freeze
└── README.md # one-command setup and usage
Repo checklist: README that runs · standalone eval script · training script · downloadable weights · restored outputs · pinned requirements. All six mandated items present.
Links & demo
GitHub: [ public link — added when repo goes public ]
Video: [ 90-second screen capture: eval.py restoring a folder in real time ]
Weights: in-repo (< 100 MB) or Hugging Face mirror
License: MIT
The demo video shows
1. fresh clone → pip install → single command
2. degraded folder in → restored folder out, with per-image latency
3. side-by-side panels + the model's own degradation read-out (σ-speckle, blur, kernel)
4. the LODO table proving OOD performance

## Slide 9
References
Papers and tools this design builds on
DRISHTI-Net · KLA i4C Hackathon · PS01
9 / 9
1. Chen et al. — “NAFNet: Nonlinear Activation Free Network for Image Restoration”, ECCV 2022. (backbone)
2. Perez et al. — “FiLM: Visual Reasoning with a General Conditioning Layer”, AAAI 2018. (degradation conditioning)
3. Wang et al. — “Real-ESRGAN: Training Real-World Blind Super-Resolution with Pure Synthetic Data”, ICCVW 2021. (degradation randomization)
4. Jiang et al. — “Focal Frequency Loss for Image Reconstruction and Synthesis”, ICCV 2021. (FFT loss term)
5. Wang et al. — “Multiscale Structural Similarity for Image Quality Assessment”, 2003. (MS-SSIM)
7. Zhang et al. — “LPIPS: The Unreasonable Effectiveness of Deep Features as a Perceptual Metric”, CVPR 2018. (metric)
8. Zamir et al. — “Restormer: Efficient Transformer for Image Restoration”, CVPR 2022. (comparison baseline)
9. Liang et al. — “SwinIR: Image Restoration Using Swin Transformer”, ICCVW 2021. (comparison baseline)
10. Yoo et al. — “CutBlur: Re-thinking Data Augmentation for Low-Level Vision”, CVPRW 2020. (anti-hallucination aug)
11. Charbonnier et al. — “Deterministic Edge-Preserving Regularization in Computed Imaging”, 1997. (robust pixel loss)
12. KLA / i4C — PS01 problem brief: data notes, out-of-range speckle behaviour, OOD test set, H100 benchmark.
Tools: PyTorch 2.x · OpenCV · NumPy · pytorch-msssim · lpips · ONNX Runtime / TensorRT · Albumentations-free (custom engine by design).