## Slide 1
KLA i4C HACKATHON · PROBLEM STATEMENT PS01
DrishtiNet
दृष्टि
Deterministic, range-safe restoration of degraded semiconductor inspection images
DRISHTI-Net = Degradation-aware Restoration via Implicit Supervision for High-fidelity Technology Inspection
TEAM DETAILS
Member name | Role in team | Focus area
[ FILL: name ] | Lead architect | Model design, training runs, experiment ladder
[ FILL: name ] | Data / loss engineer | Degradation engine, FabLoss, Day-0 audit
[ FILL: name ] | Deployment & benchmarking | eval.py, FP16/ONNX, timing harness
[ FILL: name ] | Validation & narrative | Metric suite, LODO, visuals, deck
Registration
Team name: [ FILL before PDF export ]
College: [ FILL ]
City: [ FILL ]
Contact: [ FILL ]
Track: KLA — PS01 (image restoration)
Submission format: PDF, file name TeamName_KLA_PS01 · 9 slides (this deck) · public GitHub repo linked on slide 8
DRISHTI-Net · KLA i4C Hackathon · PS01
1 / 9

## Slide 2
Problem statement — why this matters
AI-based restoration of degraded images for semiconductor inspection (KLA, PS01)
DRISHTI-Net · KLA i4C Hackathon · PS01
2 / 9
• One pixel can hide a defect. Inspection images drive pass/fail decisions at every fab stage; a speckle spike or a lost line edge can mask a killer defect and ship a bad die.
• Real inspection images arrive degraded. Random speckle, a soft Gaussian haze, and 2× downsampling (512²→256², 256²→128²) jointly destroy signal. These losses occur together, not one at a time.
• Engineers currently just live with it. Every fab pays for degraded data in escapes and re-measurements. Restoration that recovers the true image is direct yield value.
• The catch: the test set is out-of-distribution. Winning requires generalizing to unseen image sources — and doing it fast enough to inline with fab throughput.
Speckle noise
Random, grainy, multiplicative — pushes pixels BEYOND the true intensity range.
Must fix: Denoise without blurring away real structure.
Gaussian degradation
Soft, hazy, edges lose sharpness — blur and/or additive noise.
Must fix: Restore edge sharpness; no ringing artifacts.
2× resolution loss
512²→256² or 256²→128² downsampled; fine detail gone.
Must fix: Reconstruct missing detail while upscaling 2×.
The trap designed into this PS: degraded intensities can exceed the ground-truth range. Any pipeline that clips or min-max normalizes destroys exactly the information it was asked to protect.

## Slide 3
Idea description — read it, restore it, protect it
One model. One forward pass. Every shipped decision gated by a measurement.
DRISHTI-Net · KLA i4C Hackathon · PS01
3 / 9
“DRISHTI-Net restores corrupted inspection frames in a single deterministic forward pass — and it was built the way a fab qualifies a process: every candidate enhancement (FiLM degradation conditioning, synthetic-data arms, SSIM/frequency loss terms) entered a controlled ablation ladder and survived only if it beat a measured gate. The checkpoint we ship is the configuration that won.”
1 · Encode range-safely
• Two-channel encoding [x/S, log1p(x/S)], scale S fixed from the Day-0 census — never clipped
• Measured on real data: degraded pixels span [−0.28, +2.16] vs GT [0, 1] — out-of-range speckle is protected signal, not an artifact
• A degradation-parameter reader (aux head) is implemented and validated on synthetic pairs
2 · Restore deterministically
• NAF-style encoder–decoder (SimpleGate, SCA, LayerNorm — SCA placement adapted; no BatchNorm)
• One joint pass: denoise + deblur + 2× super-resolution — no cascade, no information loss between stages
• PixelShuffle learned ×2 + global bilinear residual; 3.47 M params (exact count printed from the shipped checkpoint)
3 · Protect the patterns
• Shipped objective: Charbonnier pixel loss — robust PSNR-aligned base (FabLoss V1, gate winner)
• Sobel / FFT variants were gated through isolated arms — the champion formula is the one that measured best (slides 5–6)
• Deterministic reconstruction objective, not a generative prior — minimizing the risk of synthesizing unsupported structure
Deliberately absent: diffusion / GAN (hallucination risk + fails the latency benchmark), Mixture-of-Experts and hard routing (training instability, branching latency), Mamba/SSM kernels (toolchain risk on a clean benchmark machine).
In inspection, a fabricated edge is a false defect and a smoothed scratch is an escape — we chose determinism.

## Slide 4
Proposed solution — architecture & training system
Measured Day-0 census · engineered stability · gated loss design
DRISHTI-Net · KLA i4C Hackathon · PS01
4 / 9
Input
128² / 256²
float32, native range
Input encoding
[x/S , log1p(x/S)]
2 channels · no clipping
S fixed on Day 0
Degradation conditioning
z-NORM + tanh-bounded FiLM
stability-verified over 10k steps*
shipped checkpoint: dormant
(aux head: synthetic pairs only)
NAF-style U-Net
enc [2,2,4] → mid 4 → dec [2,2,2]
SimpleGate + SCA + LayerNorm
no BatchNorm · skip-adds at 3 scales
PixelShuffle ×2
conv 32→128 · shuffle
conv 32→1
+ bilinear global residual
Restored output
256² / 512²
GT dtype & range
exact inversion
* FiLM variant verified stable (zAbs 0.46→0.25, gains pinned at the tanh bound, grad-norm decaying 0.12→0.009 over 10k iters) but did not beat the gate inside the 24 h budget — capability kept and documented; claim gated by ablation. Real KLA pairs carry no degradation labels, so the aux head is masked on real pairs by construction.
FabLoss — the metrology-aligned loss
Shipped (FabLoss V1): L = L_Charbonnier
Challenger (V2): L_Charb + 0.2·L_Sobel + 0.1·L_FFT-magnitude-consistency — 30k-iter run, gate verdict on slide 6
• Charbonnier — robust pSNR base; gradients vanish smoothly near convergence
• MS-SSIM (λ=0.5) — REJECTED from V1: a real-only arm collapsed 29.32 → 13.20 dB with erratic gradient spikes to ×232 (slide 6). Excised by measurement, not opinion
• Sobel edge + FFT magnitude consistency (L1, orthonormal) — each isolated in 5k arms, then combined in the V2 challenger
• aux — degradation-parameter regression, active on synthetic pairs only
Every λ is fixed by our ablation ladder, never assumed.
Synthetic degradation engine — fingerprinted, then honest about its role
• Speckle multiplicative, unclipped — post-downsample σ ≈ 0.157 dominant (Day-0 census of all 3,200 pairs)
• Gaussian blur + additive noise · 4 downsample-kernel families · random order (measured noise-first frequency 0.70)
• CutBlur · D4 symmetries · instrument artifacts: scan-line jitter, column banding, edge bloom
• Shipped champion trained on real pairs; synthetic arms re-queued behind the worker-seeding fix (verified 1,024/1,024 unique vectors)
We learn the degradation process, not the training images.

## Slide 5
Innovation & uniqueness — five claims, each with evidence
Novelty that survives cross-examination: every claim pairs with a measured proof
DRISHTI-Net · KLA i4C Hackathon · PS01
5 / 9
1
Range-safe encoding & output contract
Fixed-scale [x/S, log1p(x/S)] channels: degraded pixels measured up to −0.28…+2.16 (GT [0,1]) are preserved, never squashed. Output mirrors GT dtype and range exactly.
Proof: Day-0 census of all 3,200 pairs + evaluate.py round-trip of real .npy files (same name, same dtype)
2
Loss terms convicted by controlled arms, not curated by taste
Every candidate term ran isolated 5k steps from the same init on the same holdout. MS-SSIM collapsed catastrophically even with clamp + ramp active — and a Sobel control arm could not rescue it.
Proof: four-arm table (slide 6): collapses 13.20 / 13.48 dB vs stable 29.3 dB arms; erratic gradient spikes to ×232 / ×736 vs ≤0.2 in stable arms
3
Training-systems discipline (the silent-bug hunt)
A seeding bug made every dataloader worker sample identical degradations — silently weakening all synthetic arms. Found by statistical test, fixed, re-verified under Windows spawn semantics.
Proof: 1,024/1,024 unique degradation parameter vectors at 0/2/4 workers; kernel & order frequencies match the engine census
4
FiLM degradation conditioning — verified, then gated
The conditioned variant (z-norm + tanh-bounded gains) ships in the repo. The revised implementation remained stable under 10k-step telemetry, eliminating the previously observed runaway behavior — yet it did not beat the gate in budget, so the shipped checkpoint keeps conditioning dormant.
Proof: per-stage telemetry — zAbs 0.46→0.25 · gains pinned at bounds · grad-norm 0.12→0.009 (log in repo)
5
Deterministic, anti-synthesis design
A deterministic reconstruction objective rather than a generative prior — minimizing the risk of synthesizing unsupported structures (or erasing real ones). Built for metrology, not for pretty pictures.
Proof: flat-region residual σ = 0.0232 mean + worst-10% patch SSIM 0.7354 — 160 held-out frames, printed by scripts/report.py
Also engineered in: degradation-order census match (noise-first 0.70) · worst-patch metrics so blur can't hide behind global means · benchmark-hardened zero-edit evaluate.py (CPU fallback, dtype-mirroring, per-image stdout for the timing harness).

## Slide 6
Results — measured, not promised
Every number on this slide is produced by our own evaluation harness on held-out splits. No estimates.
DRISHTI-Net · KLA i4C Hackathon · PS01
6 / 9
Configuration — held-out 160 pairs, train-excluded | PSNR ↑ dB | SSIM ↑ | Loss recipe | Verdict
Champion: M3e = FabLoss V2 (best.pt, step 21,000) | 29.33 | 0.7913 | Charb + 0.2·Sobel + 0.1·FFT-mag | SHIPPED — beat gate on both
Gate-setter: M0r-v5 (best.pt, step 19,000) | 29.32 | 0.7911 | Charbonnier | baseline it beat
Ablation M3a / M3d (+ control) | 13.20 / 13.48 | 0.3257 / 0.5606 | Charb + 0.5·MS-SSIM (±Sobel) | collapse — excised
Ablation M3b | 29.31 | 0.7907 | Charb + 0.2·Sobel | safe ≠ useful
Ablation M3c | 29.29 | 0.7924 | Charb + 0.1·FFT-mag | SSIM-lean → V2 seed
All numbers from our own harness on the same held-out 160 pairs (train-excluded). Extended suite — edge-region PSNR, edge-SSIM, flat-region residual σ, worst-10%-patch SSIM, LPIPS local diagnostic, timing — from scripts/report.py on both champions (reports/M3e_30k.md and reports/M0r_v5.md in the repo).
OOD proxy — a synthetic degradation family no candidate ever trained on (all three checkpoints are real-pairs-only; LANCZOS4 corner, seed 777, paired inputs): champion 25.46 dB / 0.604 · baseline 25.56 / 0.611 · FiLM 25.56 / 0.611, within 0.11 dB — on this proxy, neither enhanced model improved over the real-only baseline. Evidence, not a prediction of the KLA test set (reports/lodo_kernel3.md).
Honesty note: margins under ~0.05 dB are within our observed run-to-run variance and are NOT claimed as significant; exact checkpoint values and full trajectories ship in the repo.
Measurement protocol
• Timing: per-image CUDA sync, steady-state trace of 800 consecutive images (median + p95, scripts/latency_trace.py) — local RTX 4060 Laptop GPU benchmark; no H100 projection
• Holdout: last 160 sorted filenames, never trained on · SSIM = our Gaussian-window implementation (consistent internal comparator)
• LPIPS: local-only diagnostic (lpips pkg, torchvision VGG weights; provenance documented) — never a gate metric
• Same zero-edit script KLA will run: evaluate.py
Degraded input
degraded input — 128² (real KLA train pair)
DRISHTI-Net output
DRISHTI-Net output — restored 256² (from outputs/restored_train)
Ground truth
ground truth — clean 256²
A — Typical held-out case: 003193 · 29.07 dB / SSIM 0.9029 B — Strongest textured held-out case: 003107 · 37.22 dB / 0.9538 C — Challenging held-out case: 003136 · 23.87 dB / 0.7097
Panels render the shipped checkpoint's actual outputs on never-trained holdout frames — deliberate SPREAD selected by measured rule: A = nearest-median PSNR · B = strongest among textured frames (Sobel-energy floor ≥ P25; near-blank frames earn trivially high PSNR and are excluded by rule, not by eye — skipped frames printed by name) · C = challenging (P10). Renders + full receipts ship in the repo (docs/panels/panels_index.txt).
A
B
C
A
B
C
A
B
C

## Slide 7
Technology & feasibility
Small model, standard stack, reproducible by design
DRISHTI-Net · KLA i4C Hackathon · PS01
7 / 9
Stack & numbers
Framework
PyTorch 2.x · bf16 mixed precision · grad-clip + probe telemetry harness
Data engine
OpenCV + NumPy · on-the-fly engine fingerprinted by the Day-0 census
Model size
3.47 M params, ~14 MB fp32 (exact count printed from the shipped checkpoint)
Inference
single pass, FP16 with automatic FP32 fallback · dtype-mirroring I/O
Latency
16.5 ms/img median · 19.2 p95 — 800 consecutive sync-timed images, SM-clock sampled (trace-verified) · 17.4 ms full-folder streaming (3,200 imgs) — RTX 4060 Laptop benchmark; no H100 projection
Training HW
RTX 4060 8 GB laptop — 0.15–0.19 s/iter @256² measured; champion 30k iters ≈ 1.5 h
Eval script
zero-edit CLI · auto CUDA→CPU · per-image stdout progress for the timing harness
Reproducibility
requirements.txt · fixed seeds logged per run · fresh-clone run gate before submit
Why this is feasible — and disciplined
• ~3.5 M-param CNN: a full 30k run is ~1.5 h on a laptop — the entire ablation ladder fit the hackathon clock
• Gate discipline: a term or variant must beat a measured gate or it is cut — MS-SSIM cut by evidence, conditioning kept dormant by evidence
• Full-frame 256² training (patch = frame), cosine LR, warmup tuned against measured instability
• evaluate.py degrades to CPU-only gracefully if the scoring machine lacks CUDA
Execution plan
D0
data census
D1
engine + audit
D2
v4 ladder: failures logged
D3
v8 revision + re-baseline
D4
champion 30k + M3 battery
D5
V2 challenger gate
D6
ship: deck + repo + demo
Hard vetoes: diffusion · MoE/hard routing · Mamba · gradient-TTA · clipping normalization · BatchNorm · any unmeasured number.

## Slide 8
GitHub repository & demo
A reviewer clones the repo and runs inference without contacting us
DRISHTI-Net · KLA i4C Hackathon · PS01
8 / 9
Repository — github.com/[team]/drishti-net
├── data/ # loaders + census-fingerprinted degradation engine
├── models/ # DRISHTI-Net NAF-style net + FiLM variant
├── losses/ # FabLoss: Charb shipped; Sobel/FFT arms; MS-SSIM kept as ablation
├── utils/ # metrics: Gaussian SSIM, edge/flat/worst-patch, LPIPS diagnostic
├── scripts/ # day0_audit · report.py · loss unit tests · ladder runner
├── weights/ # drishti_net.pt — THE champion (exactly one model file)
├── tests/smoke/ # smoke weights (dev-only placeholder, power-on self-test)
├── outputs/ # demo restores + panels (full 3,200-file set reproduces with one command — too large for git)
├── reports/ # report.py + lodo_eval evidence (json/md, both champions)
├── docs/ # audit report · reviewer evidence · MASTER_SPEC decision log
├── evaluate.py # MANDATORY: zero-edit CLI inference
├── train.py # the full ladder with probe telemetry
└── README.md + requirements.txt
Repo checklist: README that runs · standalone eval script · training script · downloadable weights · restored outputs · pinned requirements. All six mandated items present.
Links & demo
GitHub: [ FILL — repo goes public at submission ]
Video: [ FILL — 90-second capture: fresh clone → evaluate.py restoring a folder ]
Weights: in-repo (~14 MB, under the 100 MB limit)
License: MIT
The demo video shows
1. fresh clone → pip install -r requirements.txt → a single command
2. folder of degraded .npy in → restored folder out, with per-image stdout progress + latency line
3. before/after panels rendered from outputs/restored_train on the real train set
4. reports/*.md table: PSNR / SSIM / edge / flat-region σ / worst-patch / LPIPS + device-tagged timing

## Slide 9
References
Papers and tools this design builds on
DRISHTI-Net · KLA i4C Hackathon · PS01
9 / 9
1. Chen et al. — “NAFNet: Nonlinear Activation Free Networks for Image Restoration”, ECCV 2022. (blocks are a NAF-style variant: SCA placement adapted — deliberate)
2. Perez et al. — “FiLM: Visual Reasoning with a General Conditioning Layer”, AAAI 2018. (conditioning variant, stability-verified)
3. Wang et al. — “Real-ESRGAN: Training Real-World Blind SR with Pure Synthetic Data”, ICCVW 2021. (degradation randomization)
4. Ledig et al. — “Photo-Realistic Single Image SR Using a GAN”, CVPR 2017. (global residual learning — our bilinear add-back)
5. Wang et al. — “Multiscale Structural Similarity for Image Quality Assessment”, 2003. (evaluated in our ladder; rejected at λ=0.5 by measured collapse)
6. Charbonnier et al. — “Deterministic Edge-Preserving Regularization in Computed Imaging”, IEEE TIP 1997. (shipped pixel loss)
7. Zhang et al. — “LPIPS: The Unreasonable Effectiveness of Deep Features as a Perceptual Metric”, CVPR 2018. (local-only diagnostic)
8. Zamir et al. — “Restormer”, CVPR 2022 · Liang et al. — “SwinIR”, ICCVW 2021. (related architectures considered; a compact CNN chosen for determinism + benchmark latency)
9. Yoo et al. — “CutBlur: Re-thinking Data Augmentation for Low-Level Vision”, CVPRW 2020. (augmentation)
10. Ronneberger et al. — “U-Net”, MICCAI 2015. (encoder–decoder + skip connections)
11. KLA / i4C — PS01 problem brief: data notes, out-of-range speckle behaviour, OOD test set, H100 benchmark.
Tools: PyTorch 2.x · OpenCV · NumPy · pytorch-msssim (ablation arms only) · lpips (diagnostic only) · custom degradation engine by design.